## Slide 1
TEAM FOXTROT
SAFEPAWS
ECE - Capstone Design 1
FINAL DESIGN REVIEW

## Slide 2
Overview
Introduction
Design Overview
Conclusion
User Journey
Subsystems
Questions?
Competitive Advantage
Future Work
References

## Slide 3
Nathan Phan
Victor Gonzalez
Data Systems
Terry Jenkins
Team Lead / Sensors
Communications
SafePaws
Our
Team

## Slide 4
Clayton Lott
DeArirreis Vance
Faculty Advisor
Vuk Marojevic
Power Systems
Software
SafePaws
Our
Team

## Slide 5
Problem 02
Problem 03
SafePaws
The Problem
Owners can lead busy lives leaving limited time for continuous monitoring of their dogs' health.
Problem 01
Veterinary visits can be time-consuming, costly, and may not offer timely insights into a pet's health.
Current pet health monitoring products on the market are complex and expensive, limiting accessibility for some owners.

## Slide 6
SafePaws
Our Solution
Less Expensive
than Competitors
2
Continuous & Convenient Monitoring
Pet
Comfort
Design
Notes: user experience - cost, ease of use
functionality - alerts, continuous, app
performance - data accurate, battery life

## Slide 7
Competition
DogLeggs [1]
  Cost
  Specialized Use
  Limited Connectivity
PetPace [2]
  Expensive Initial Cost
  Subscription to Premium Features
SafePaws

## Slide 8
SafePaws
4
Design Overview

## Slide 9
04
01
Subsystems
SafePaws
03
02
5

## Slide 10
Arduino Uno REV3
Advantages: [3]
  Low-power requirement
  Support for a wide range of peripherals
    SD card read/write
    WiFI/Bluetooth
  Digital/analog sensor support
  Well-supported software library
    SD-FATLIB (FAT16/FAT32 file systems)
    Arduino BLE (Bluetooth), ConnectionHandler (WiFI)
Alternatives considered:
  Basys Board
  Raspberry Pi
Controller
SafePaws
Arduino Uno REV3
https://store.arduino.cc/products/arduino-uno-rev3

## Slide 11
SafePaws
Communications
File Storage & Wireless Connectivity
SD Card
Bluetooth
DSD TECH HM-10 M Bluetooth 4.0 LE
Zittop SD Card Read/Write Module
  100GB Read/Write Speed Support
  4-wire connectivity
  Bluetooth 4.0 support
  4-wire connectivity
Notes: not completed

## Slide 12
Pulse Sensor (Photoplethysmogram)
  PPG utilizes a light-emitting diode to detect changes in blood volume. [4]
  The vest uses 2 Pulse Sensors for more accurate readings.
  Ease of use.
SafePaws
Sensors
DS18B20 (Digital Thermometer)
  DS18B20 uses a feature called the one-wire interface. [5]
  This thermometer has a wider temperature range than alternatives.
  This sensor allows for more accurate readings.
Notes: ease of use?

## Slide 13
SafePaws
Sensors
Notes: slide for sensor demonstration

## Slide 14
  7.4V 2600mAh lithium-ion battery
  Arduino steps down usage to 5-volt
  37 hours of usable battery life (goal of 24 hours)
  Removable battery
  USB rechargeable
Power
SafePaws

## Slide 15
Mobile Application
Easy to Use
Modern Design
Cross-Platform Compatibility
User Friendly
SafePaws

## Slide 16
SafePaws
Snapshot
Notes: slide for app demonstration

## Slide 17
SafePaws
Upcoming
Implementation into vest
Removal of LCD
Right now the subsystems are configured loosely; so the next step is to integrate them into the vest in such a way as to meet our constraints.
The LCD is only there for testing purposes; it will not be integrated into the final design as the needed information will be transmitted to the mobile app.
App Development
The application software is still being developed to reach launch-ready.

## Slide 18
Challenges
  Teamwork
  Design
Limitations
  Time
  Money
  Lack of knowledge
Lessons Learned
  Coding
  Oral Communication
  Hardware integration
Reflections

## Slide 19
[1] “Dog Leg Wraps, Braces, & Carpal Support | Hygroma Treatment Solutions,” dogleggs.com. https://www.dogleggs.com/ (accessed Sep. 01, 2023).
{2] “How it works - PetPace,” PetPace.com, https://petpace.com/how-it-works/ (accessed Sep. 01, 2023).
[3] “Arduino Uno R3 Specification Sheet.” Arduino Documentation. https://docs.arduino.cc/hardware/uno-rev3 (accessed Oct. 20, 2023).
[4] “In-Depth: Detect, Measure & Plot Heart Rate Using Pulse Sensor & Arduino,”
LastMinuteEngineers.com. https://lastminuteengineers.com/pulse-sensor-arduino-tutorial/ (accessed Nov 8, 2023)
[5] “Waterproof 1-Wire DS18B20 Digital Temperature Sensor,” Adafruit.com.
https://www.adafruit.com/product/381?gclid=CjwKCAjws9ipBhB1EiwAccEi1I_Cpjkz6gxzXgaTveIUXc
OG1HRZNsbkSlXBfyg8ZbmgEaWvQ2WrZRoCuzIQAvD_BwE (accessed Nov 8, 2023).
References
Notes: references not completed